## Slide 1: Number System and Code Conversion
Dr. Manju Khurana
Assistant Professor, CSED
TIET, Patiala
manju.khurana@thapar.edu

## Slide 2: Number System :: The Basics

## Slide 3: Number System :: The Basics
We are accustomed to using the so-called decimal number system.
  Ten digits :: 0,1,2,3,4,5,6,7,8,9
  Every digit position has a weight which is a power of 10.
  Base or radix is 10.
Example:
  = 2 x 102 + 3 x 101 + 4 x 100
  250.67 = 2 x 102 + 5 x 101 + 0 x 100 + 6 x 10-1 + 7 x 10-2

## Slide 4: Binary Number System
Two digits:
  0 and 1.
  Every digit position has a weight which is a power of 2.
  Base or radix is 2.
Example:
  110 = 1 x 22 + 1 x 21 + 0 x 20
  101.01 = 1 x 22 + 0 x 21 + 1 x 20 + 0 x 2-1 + 1 x 2-2

## Slide 5: Counting with Binary Numbers
0
1
10
11
100
101
110
111
1000
.

## Slide 6: Multiplication and Division with base
Multiplication with 10 (decimal system)
435 x 10 = 4350
Multiplication with 10 (=2 ) (binary system)
1101 x 10 = 11010
Division by 10 (decimal system)
435 / 10 = 43.5
Division by 10 (=2) (binary system)
1101 / 10 = 110.1
Left Shift and add
zero at right end
Right shift and drop
right most digit or
shift after decimal
point

## Slide 7: Adding two bits
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10
carry
1 1 1 0
1 0 1 1
+ 1 1 1 0
1 1 0 0 1
Carries

## Slide 8: Binary addition: Another example
1 1 0 0 (Carries)
1 1 0 1
+ 1 1 0 0
1 1 0 0 1 (Sum)
The initial carry
in is implicitly 0
most significant
bit (MSB)
least significant
bit (LSB)

## Slide 9: Binary-to-Decimal Conversion
Each digit position of a binary number has a weight.
  Some power of 2.
A binary number:
  B = bn-1 bn-2 …..b1 b0 . b-1 b-2 ….. b-m
Corresponding value in decimal:
  D =  bi 2i
i = -m
n-1

## Slide 10: Examples
101011  1x25 + 0x24 + 1x23 + 0x22 + 1x21 + 1x20
= 43
(101011)2 = (43)10
.0101  0x2-1 + 1x2-2 + 0x2-3 + 1x2-4
= .3125
(.0101)2 = (.3125)10
101.11  1x22 + 0x21 + 1x20 + 1x2-1 + 1x2-2
5.75
(101.11)2 = (5.75)10

## Slide 11: Binary-to-Octal Conversion
Conversion of a binary number to an octal number is the reverse of the octal-to-binary conversion.
Let’s convert the following binary numbers to octal:
1 1 0 1 0 1 1 0 1 1 1 1 0 0 1
6 5 = 65 5 7 1 = 571

## Slide 12: Binary-to-Octal Conversion
Group bits into sets of threes, starting from the RHS.
Convert each set to octal digits.

## Slide 13: Binary-to-Hexadecimal Conversion
For the integer part,
  Scan the binary number from right to left.
  Translate each group of four bits into the corresponding hexadecimal digit.
    Add leading zeros if necessary.
For the fractional part,
  Scan the binary number from left to right.
  Translate each group of four bits into the corresponding hexadecimal digit.
    Add trailing zeros if necessary.

## Slide 14: Example
(1011 0100 0011)2 = (B43)16
(10 1010 0001)2 = (2A1)16
(.1000 010)2 = (.84)16
(101 . 0101 111)2 = (5.5E)16

## Slide 15: Binary-to-Hexadecimal Conversion
Group bits into sets of fours, starting from the RHS.
Convert each set to hexadecimal digits.

## Slide 16: Decimal-to-Binary Conversion
Consider the integer and fractional parts separately.
For the integer part,
  Repeatedly divide the given number by 2, and go on accumulating the remainders, until the number becomes zero.
  Arrange the remainders in reverse order.
For the fractional part,
  Repeatedly multiply the given fraction by 2.
    Accumulate the integer part (0 or 1).
    If the integer part is 1, chop it off.
  Arrange the integer parts in the order they are obtained.

## Slide 17: Example 1 :: 239
239
2 119 --- 1
59 --- 1
2 29 --- 1
14 --- 1
2 7 --- 0
3 --- 1
2 1 --- 1
2 0 --- 1
(239)10 = (11101111)2

## Slide 18: Example 2 :: 64
64
2 32 --- 0
16 --- 0
2 8 --- 0
4 --- 0
2 2 --- 0
1 --- 0
2 0 --- 1
(64)10 = (1000000)2

## Slide 19: Example 3 :: .634
.634 x 2 = 1.268
.268 x 2 = 0.536
.536 x 2 = 1.072
.072 x 2 = 0.144
.144 x 2 = 0.288
:
:
(.634)10 = (.10100……)2

## Slide 20: Example 4 :: 37.0625
(37)10 = (100101)2
(.0625)10 = (.0001)2
(37.0625)10 = (100101 . 0001)2

## Slide 21: Decimal-to-Octal Conversion
A method of converting a decimal number to an octal number is the repeated division-by-8 method, which is similar to the method used in the conversion of decimal numbers to binary or to hexadecimal.
Let’s convert the decimal number 359 to octal. Each successive division by 8 yields a remainder that becomes a digit in the equivalent octal number. The first remainder generated is the least significant digit (LSD).
359 = 44.875 0.875 x 8 = 7 (LSD)
8
44 = 5.5 0.5 x 8 = 4
8
5 = 0.625 0.625 x 8 = 5 (MSD)
8
The number is 547.

## Slide 22: Decimal-to-Octal Conversion
Divide the number and every subsequent quotient by eight and keep track of the remainder.

## Slide 23: Decimal-to-Hexadecimal Conversion
Repeated division of a decimal number by 16 will produce the equivalent hexadecimal number, formed by the remainders of the divisions. The first remainder produced is the least significant digit (LSD). Each successive division by 16 yields a remainder that becomes a digit in the equivalent hexadecimal number. When a quotient has a fractional part, the fractional part is multiplied by the divisor to get the remainder.

## Slide 24
Convert the decimal number 650 to hexadecimal by repeated division by 16.
650 = 40.625 0.625 x 16 = 10 = A (LSD)
16
40 = 2.5 0.5 x 16 = 8 = 8
16
2 = 0.125 0.125 x 16 = 2 = 2 (MSD)
16
The hexadecimal number is 28A
Decimal-to-Hexadecimal Conversion

## Slide 25: Decimal-to-Hexadecimal Conversion
Divide the number and every subsequent quotient by sixteen and keep track of the remainder.

## Slide 26: Hexadecimal Number System
A compact way of representing binary numbers.
16 different symbols (radix = 16).
  0  0000 8  1000
  1  0001 9  1001
  2  0010 A  1010
  3  0011 B  1011
  4  0100 C  1100
  5  0101 D  1101
  6  0110 E  1110
  7  0111 F  1111

## Slide 27: Hexadecimal-to-Binary Conversion
Translate every hexadecimal digit into its 4-bit binary equivalent.
Examples:
  (3A5)16 = (0011 1010 0101)2
  (12.3D)16 = (0001 0010 . 0011 1101)2
  (1.8)16 = (0001 . 1000)2

## Slide 28: Hexadecimal-to-Decimal Conversion
One way to find the decimal equivalent of a hexadecimal number is to first convert the hexadecimal number to binary and then convert from binary to decimal.
Example:
(1C)16 = (0001 1100)2 = 24 + 2³ + 2² = 16 + 8 + 4 = 28

## Slide 29: Hexadecimal-to-Octal Conversion
Use binary as an intermediary.

## Slide 30: Octal Numbers
Like the hexadecimal system, the octal system provides a convenient way to express binary numbers and codes.
However, it is used less frequently than hexadecimal in conjunction with computers and microprocessors to express binary quantities for input and output purposes.
The octal system is composed of eight digits, which are:
0, 1, 2, 3, 4, 5, 6, 7
To count above 7, begin another column and start over:
10, 11, 12, 13, 14, 15, 16, 17, 20, 21 and so on.
Counting in octal is similar to counting in decimal, except that the digits 8 and 9 are not used.

## Slide 31: Octal-to-Decimal Conversion
Since the octal number system has a base of eight, each successive digit position is an increasing power of eight, beginning in the right-most column with 80. The evaluation
Of an octal number in terms of its decimal equivalent is accomplished by multiplying each digit by its weight and summing the products.
Let’s convert octal number 2374 in decimal number.
Weight 8³ 8² 81 80
Octal number 2 3 7 4
2374 = (2 x 8³) + (3 x 8²) + (7 x 81) + (4 x 80)=1276

## Slide 32: Octal-to-Binary Conversion
Because each octal digit can be represented by a 3-bit binary number, it is very easy to convert from octal to binary..
Octal/Binary Conversion
Octal Digit 0 1 2 3 4 5 6 7
Binary 000 001 010 011 100 101 110 111
Let’s convert the octal numbers 25 and 140.
2 5 1 4 0
010 101 001 100 000

## Slide 33: Octal-to-Hexadecimal Conversion
Use binary as an intermediary.

## Slide 34: Unsigned Binary Numbers
An n-bit binary number
  B = bn-1bn-2 …. b2b1b0
    2n distinct combinations are possible, 0 to 2n-1.
For example, for n = 3, there are 8 distinct combinations.
  000, 001, 010, 011, 100, 101, 110, 111
Range of numbers that can be represented
  n=8  0 to 28-1 (255)
  n=16  0 to 216-1 (65535)
  n=32  0 to 232-1 (4294967295)

## Slide 35: Signed Integer Representation
Many of the numerical data items that are used in a program are signed (positive or negative).
  Question:: How to represent sign?
Three possible approaches:
  Sign-magnitude representation
  One’s complement representation
  Two’s complement representation

## Slide 36: Sign-magnitude Representation
For an n-bit number representation
  The most significant bit (MSB) indicates sign
    0  positive
    1  negative
  The remaining n-1 bits represent magnitude.
b0
b1
bn-2
bn-1
Magnitude
Sign

## Slide 37: Representation and ZERO
Range of numbers that can be represented:
  Maximum :: + (2n-1 – 1)
  Minimum ::  (2n-1 – 1)
A problem:
  Two different representations of zero.
    +0  0 000….0
    -0  1 000….0

## Slide 38: One’s Complement Representation
Basic idea:
  Positive numbers are represented exactly as in sign-magnitude form.
  Negative numbers are represented in 1’s complement form.
How to compute the 1’s complement of a number?
  Complement every bit of the number (10 and 01).
  MSB will indicate the sign of the number.
    0  positive
    1  negative

## Slide 39: Example :: n=4
0000  +0
0001  +1
0010  +2
0011  +3
0100  +4
0101  +5
0110  +6
0111  +7
1000  -7
1001  -6
1010  -5
1011  -4
1100  -3
1101  -2
1110  -1
1111  -0
To find the representation of -4, first note that
+4 = 0100
-4 = 1’s complement of 0100 = 1011

## Slide 40: One’s Complement Representation
Range of numbers that can be represented:
  Maximum :: + (2n-1 – 1)
  Minimum ::  (2n-1 – 1)
A problem:
  Two different representations of zero.
    +0  0 000….0
    -0  1 111….1
Advantage of 1’s complement representation
  Subtraction can be done using addition.
  Leads to substantial saving in circuitry.

## Slide 41: Two’s Complement Representation
Basic idea:
  Positive numbers are represented exactly as in sign-magnitude form.
  Negative numbers are represented in 2’s complement form.
How to compute the 2’s complement of a number?
  Complement every bit of the number (10 and 01), and then add one to the resulting number.
  MSB will indicate the sign of the number.
    0  positive
    1  negative

## Slide 42: Example :: n=4
0000  +0
0001  +1
0010  +2
0011  +3
0100  +4
0101  +5
0110  +6
0111  +7
1000  -8
1001  -7
1010  -6
1011  -5
1100  -4
1101  -3
1110  -2
1111  -1
To find the representation of, say, -4, first note that
+4 = 0100
-4 = 2’s complement of 0100 = 1011+1 = 1100

## Slide 43: IEEE Standard 754 Floating Point Numbers
The IEEE Standard for Floating-Point Arithmetic (IEEE 754) is a technical standard for floating-point computation which was established in 1985 by the Institute of Electrical and Electronics Engineers (IEEE).
IEEE 754 numbers are divided into two representation based on the three components (Sign, Exponent and Mantissa):
Single precision (32-bit)
Double precision (64-bit)

## Slide 44
IEEE 754 has 3 basic components:
The Sign of Mantissa – This is as simple as the name. 0 represents a positive number while 1 represents a negative number.
The Biased exponent – The exponent field needs to represent both positive and negative exponents. A bias is added to the actual exponent in order to get the stored exponent.
The Normalised Mantissa – The mantissa is part of a number in scientific notation or a floating-point number, consisting of its significant digits. Here we have only 2 digits, i.e. 0 and 1. So a normalised mantissa is one with only one 1 to the left of the decimal.

## Slide 45: IEEE 754 Single precision (32-bit)
The IEEE-754 single precision floating point standard uses 1-bit for sign an 8-bit exponent (with a bias of 127) and a 23-bit significand.

## Slide 46: IEEE 754 double precision (64-bit)
The IEEE-754 double precision standard uses 1-bit for sign and 11-bit exponent (with a bias of 1023) and a 52-bit significand.